## Slide 1: Multi-GPU Solutions of Geophysical PDEs with Radial Basis Function-generated Finite Differences
Evan F. Bollig
Nov 6th, 2013
499 DSL, 4:30 pm – 6:30 pm

## Slide 2: Acknowledgements
This work is supported in part by NSF awards DMS-#0934331 (FSU), DMS-#0934317 (NCAR) and ATM-#0602100 (NCAR).
Computational resources provided by:
  Keeneland Computing Facility at the Georgia Institute of Technology (NSF Contract OCI-0910735)

## Slide 3: Investigation Focus
Notes: Topics covered in this defense: a) the application of a recent numerical method (barely cuts into the numerical method domain. b) a distributed implementation of RBF-FD that runs on multi-GPUs (heavy into the hardware and software). c) neighbor query algorithm (software)

## Slide 4: Overview
Preliminaries
  Introduction to GPUs
  Introduction to RBF-FD
  Code Verification Details
A Fixed-Grid Method for RBF Methods
  Space Filling Curves and Node Ordering
  Lasting Impacts on Performance
Single GPU RBF-FD
Targeting Multi-GPU Clusters
  MPI Tuning
  Overlapping Communication and Computation
Conclusions
Notes: Introduction to RBF methods (beyond RBF-FD)?

## Slide 5: Why GPUs?
Massive parallelism
High GFLOP/sec
Fast Memory
Images courtesy of NVidia
Notes: Since the early 2000’s frequency scaling is no longer an option
Parallelism is mandatory to continue with Moore’s law.

## Slide 6: How to Target GPUs?
CUDA
  Widely used
OpenCL Language
  Functional portability (CPUs and GPUs)
  Similar model as CUDA

## Slide 7: GPU Memory Model
Notes: GPU loads memory in 128byte segments. Align on those for best register density.

## Slide 8: Target: GPU Cluster
Keeneland Initial Delivery (KID) System
  360 NVidia M2070
  240 CPUs, 12 threads each
Cascade
  32 NVidia M2070
  8 NVidia K20

## Slide 9: Multi-GPU Concerns
How to partition and distribute our problem?
Faster computation increases relative cost of communication. Can it be amortized/hidden?
Multi-GPU OpenCL requires device  host copies. Can they be hidden?

## Slide 10: What is an RBF?
A radially symmetric function centered at
Notes: Note the support parameter

## Slide 11: RBF-Interpolation
Notes: Arise by enforcing

## Slide 12: Pros/Cons of RBF Methods
Pros
  Function the same in any dimension
  Operate on unstructured meshes
  High order convergence
  Large time-steps
Cons
  Support parameter,
    Uncertainty Relation (Schaback, 1995)
    Can be overcome with RBF-QR (Fornberg and Piret, 2007), RBF-GA (Fornberg, Lehto and Powell, 2013)

## Slide 13: Stencils

## Slide 14: RBF-generated Finite Differences (RBF-FD)
Classical FD (1-D*):
*Nonsingularity lost in 2-D; compose weights across dimensions
RBF-FD (d-D):

## Slide 15: Differentiation Matrix
Sparse Matrix
  n nonzeros per row (stencil size)
  Unsymmetric (unique weights per row)
Sparse Matrix Vector (SpMV) multiply to get derivative across full domain

## Slide 16: Multiple Linear Operators
Solve for weights with LAPACK dgesv or other efficient direct solver
Analytically apply operators to the RBF or compose operators like classical FD

## Slide 17: Some Weight Operators
First and Second Derivatives:
Cartesian Gradient:
Cartesian Laplacian:

## Slide 18: RBF-FD for Time-Dependent PDEs
Assume an input grid is provided.
We focus on stencil generation, decomposition and the Application Phase.

## Slide 19: Related Work on Multi-GPU
Notes: RBF OpenMP: \cite{Kosec2008} happy with 1.85x speedup using two cores
RBF MPI: \cite{Divo2005, Divo2007, Ingber2003,Ingber2004,Yokota2010}
Divo and Kassab: 10 compute nodes, then 36. Solving conjugate heat transfer problems.
Ingber: 3D diffusion equations up to 64 nodes
Yokota: RBF interpolation as component of PDE solve
RBF CUDA: \cite{Schmidt2009a,Schmidt2009b,Gumerov2007a, Gumerov2007b}
Schmidt global rbf collocation (dense matrix)
Gumerov rbf interpolation inside FMM method (dense matrix)

## Slide 20: Verification
Hyperbolic form
Hyperviscosity

## Slide 21: Grids on Unit Sphere
Maximum Determinant (MD)
Icosahedral (Geodesic) Grid
Spherical Centroidal Voronoi Tessellation

## Slide 22: Hyperviscosity
Function
Terms
Scaling

## Slide 23: Cosine Bell
Formula, Input, Solution

## Slide 24: Cosine Bell Convergence
(left) HV parameter table
(left bottom) Eigenvalue before and after tiles
(right) Convergence plot

## Slide 25: Vortex Roll-Up

## Slide 26: Neighbor Query

## Slide 27: kD-Tree

## Slide 28: Fixed Grid

## Slide 29: Fixed Grid Improvements

## Slide 30: Domain Decomposition
Restricted Additive Schwarz Method
Graph partitioning with METIS for load balancing (Karypis and Kumar, 1999)
  Requires symmetric adjacency matrix:

## Slide 31: Load Balancing with METIS
Load balancing impacts parallel gains:

## Slide 32: Node Ordering and Index Sets
Global Index Space
Local Index Space

## Slide 33: Data Movement for Multi-GPU

## Slide 34: Multi-CPU Weak Scaling
BEFORE (MPI_Alltoallv)
Tuned on Itasca (UMN)
  1,134 HP ProLiant blade servers
  2x quad-core Xeon 5660 (“Nehalem EP”) processors per node
N=1603 nodes
Impact on performance for fixed problem size per processor

## Slide 35: MPI Stages

## Slide 36: Multi-CPU Weak Scaling
2x-5x improvement at p=1024 processors
Larger Np per processor would hide growth
METIS load balancing fails for p=1024, n=17:
TUNING STEPS
AFTER

## Slide 37: Multi-CPU Strong Scaling
Fixed global problem size with decreasing workloads
MPI_Alltoallv is 2x faster when operating on one node. Slower otherwise.
Near linear (ideal) scaling.
BEFORE
AFTER
Notes: 2-way fat-tree network
8 cores is a leaf and communicate via shared memory.
Groups of 16 nodes connect via QDR InfiniBand to \emph{leaf switches} at the second level of the tree.
All leaf switches are in turn connected to two director nodes via 4x QDR InfiniBand.
The topology exhibits 8:1 contention between nodes of the same leaf and additional 2:1 contention between leaf switches \cite{ItascaTuning}.
Our implementation of RBF-FD does not detect or adjust to network topology, so network contention may inflate communication times. Tuning for the network topology is reserved for future work.

## Slide 38: Strong Scaling Efficiency and Communication Overlap
Efficiency:
Visible Communication Time:

## Slide 39: Multi-CPU Summary
Strong scaling
  Scales well aside from effects of contention IB network and insufficient problem size for large p.
Weak scaling
  Code scales well for small stencil sizes.
  Larger Np necessary to hide increasing cost of communication.
Future work:
  Align messages properly for best performance
  Possible FMM approach to limit communication between subddomains (Yokota et al. 2010)

## Slide 40: Why use the GPU?
Performance success stories from Kepler/Fermi
High TFLOP/sec count

## Slide 41: OpenCL
Comparison to CUDA
Functional Portability
Work items, work-groups, NDRange (NVIdia OpenCL manual)

## Slide 42: OpenCL vs CUDA
Diagram from Prospectus comparing hardware levels

## Slide 43: Custom Kernels
RK4 design
  Eval + Advance
  Input to each kernel

## Slide 44: Vortex Performance (Keeneland)

## Slide 45: Cosine Bell Performance
Adds one SpMV operation, but does not double performance. Question is why?

## Slide 46: Roofline Model
The roofline model predicts MAXIMUM possible performance based on the operational intensity
SpMV is only OI(1/4)

## Slide 47: How do we improve Memory-Bound Applications?
More memory compression
  ELL format
  BELL, SELL, SBELL
Fewer memory loads
  Ordering
  Register packing (non-zero condensation)
More operations (cite Erlebacher, Saule, Flyer, Bollig)

## Slide 48: Memory Compression (Format Comparison)
Figure comparing formats
Give expressions for the number of memloads

## Slide 49: Performance Comparison
N=50 format comparison figure
ELL comparison figure
Any data to compare to in related work (Rupp?, clSpMV)

## Slide 50: Future Improvements for Single GPU
clSpMV formats show potential to get 50+GFLOPs when running in single precision
What is the translation to double precision (FERMI and K20)

## Slide 52: Performance Portability? Intel Phi
High level intel phi architecture diagram
Achieved

## Slide 53: Intel Phi Comparison
Achieved GFLOP/sec on Intel Phi

## Slide 54: Performance Expectations for the GPU

## Slide 55: Achieved Performance
Cosine Bell and Vortex Roll-up

## Slide 56: SpMV Optimizations
VCL Data

## Slide 57: Overlap

## Slide 58: Limitations of I/O Hubs

## Slide 59: Achieved GFLOP/sec

## Slide 60: Conclusions

## Slide 61: Community Outreach

## Slide 62: Current and Future Work
Return to CUDA
  CUDA v5.5 features supports MPI with GPUDirect®
SpMV Improvements:
  Auto-tuned kernels with clSpMV (Su and Keutzer 2012)
  New formats:
    BELL, SELL, SBELL (Su and Keutzer 2012)
    ELLPACK-R, pJDS, etc. (Kreutzer et al. 2012)
  Applications with Multi-Matrix SpMM (Erlebacher et al. 2013)
Multiple subdomains per GPU (to saturate Fermi and Kepler cards and overlap computation)

## Slide 63: Continued and Future Work II
Intel Phi vs NVidia Kepler
  Latest hardware from Nvidia?
Multi-GPU preconditioned GMRES solutions of RBF-FD for Stokes flow
  Core operation of GMRES: SpMV
  Current work is incomplete
with RBF-GA

## Slide 64: Questions?
Remember: this is research. If we had all the answers we wouldn’t be doing it.

## Slide 67: Extras

## Slide 68: RBF-GA (Preliminary Results)