## Slide 1: Multi-GPU Solutions of Geophysical PDEs with Radial Basis Function-generated Finite Differences
Evan F. Bollig
Nov 6th, 2013
499 DSL, 4:30 pm – 6:30 pm

## Slide 2: Acknowledgements
This work is supported in part by NSF awards DMS-#0934331 (FSU), DMS-#0934317 (NCAR) and ATM-#0602100 (NCAR).
Computational resources provided by:
  Keeneland Computing Facility at the Georgia Institute of Technology (NSF Contract OCI-0910735)

## Slide 3: Investigation Focus
Notes: Topics covered in this defense: a) the application of a recent numerical method (barely cuts into the numerical method domain. b) a distributed implementation of RBF-FD that runs on multi-GPUs (heavy into the hardware and software). c) neighbor query algorithm (software)

## Slide 4: Overview
Preliminaries
  Introduction to GPUs
  Introduction to RBF-FD
  Code Verification Details
A Fixed-Grid Method for RBF Methods
  Space Filling Curves and Node Ordering
  Lasting Impacts on Performance
Single GPU RBF-FD
Targeting Multi-GPU Clusters
  MPI Tuning
  Overlapping Communication and Computation
Conclusions
Notes: Introduction to RBF methods (beyond RBF-FD)?

## Slide 5: Why GPUs?
Massive parallelism
High GFLOP/sec
Fast Memory
Images courtesy of NVidia
Notes: Since the early 2000’s frequency scaling is no longer an option
Parallelism is mandatory to continue with Moore’s law.

## Slide 6: How to Target GPUs?
CUDA
  Widely used
OpenCL Language
  Functional portability (CPUs and GPUs)
  Similar model as CUDA

## Slide 7: GPU Memory Model
Notes: GPU loads memory in 128byte segments. Align on those for best register density.

## Slide 8: OpenCL Event Queues
Queues allow non-blocking kernel launches
Concurrent kernel execution (on Fermi and Kepler GPUs)
Shared memory pool between queues.
Image courtesy of Gerstmann, 2009. Advanced OpenCL Event Model Usage (tutorial slides)

## Slide 9: Target: GPU Cluster
Keeneland Initial Delivery (KID) System
  360 NVidia M2070
  240 CPUs, 12 threads each
Cascade
  32 NVidia M2070
  8 NVidia K20

## Slide 10: Multi-GPU Concerns
How to partition and distribute our problem?
Faster computation increases relative cost of communication. Can it be amortized/hidden?
Multi-GPU OpenCL requires device  host copies. Can they be hidden?

## Slide 11: What is an RBF?
A radially symmetric function centered at
Notes: Note the support parameter

## Slide 12: RBF-Interpolation
Notes: Arise by enforcing

## Slide 13: Pros/Cons of RBF Methods
Pros
  Function the same in any dimension
  Operate on unstructured meshes
  High order convergence
  Large time-steps
Cons
  Support parameter,
    Uncertainty Relation (Schaback, 1995)
    Can be overcome with RBF-QR (Fornberg and Piret, 2007), RBF-GA (Fornberg, Lehto and Powell, 2013)

## Slide 14: RBF-generated Finite Differences (RBF-FD)
Classical FD (1-D*):
*Nonsingularity lost in 2-D; compose weights across dimensions
RBF-FD (d-D):

## Slide 15: What Kind of Stencils?

## Slide 16: Differentiation Matrix (DM)
Sparse Matrix
  n-nonzeros per row (stencil size)
  Unsymmetric (unique weights per row)
Sparse Matrix Vector (SpMV) multiply to get derivative across full domain

## Slide 17: Multiple Linear Operators
Solve for weights with LAPACK dgesv or other efficient direct solver
Analytically apply operators to the RBF or compose operators like classical FD

## Slide 18: Some Weight Operators
First and Second Derivatives:
Cartesian Gradient:
Cartesian Laplacian:

## Slide 19: RBF-FD for Time-Dependent PDEs
Assume an input grid is provided.
We focus on stencil generation, decomposition and the Application Phase.

## Slide 20: Unit Sphere Test Grids
Maximum Determinant (MD)
Icosahedral (Geodesic) Grid
Spherical Centroidal Voronoi Tessellation

## Slide 21: Related Work on Multi-GPU
Notes: RBF OpenMP: \cite{Kosec2008} happy with 1.85x speedup using two cores
RBF MPI: \cite{Divo2005, Divo2007, Ingber2003,Ingber2004,Yokota2010}
Divo and Kassab: 10 compute nodes, then 36. Solving conjugate heat transfer problems.
Ingber: 3D diffusion equations up to 64 nodes
Yokota: RBF interpolation as component of PDE solve
RBF CUDA: \cite{Schmidt2009a,Schmidt2009b,Gumerov2007a, Gumerov2007b}
Schmidt global rbf collocation (dense matrix)
Gumerov rbf interpolation inside FMM method (dense matrix)

## Slide 22: Verification
Solve hyperbolic equations with DMs of the form:
Apply hyperviscosity (Fornberg and Lehto, 2011) to filter spurious eigenmodes
  Operator:
  Applied as:
  With scaling:
Tuned hyperviscosity parameters are based on trial and error

## Slide 23: Support Parameter

## Slide 24: Vortex Roll-Up
Purpose: Spin a fluid into two diametrically opposed but stationary vortices.
Solve with Method of Lines:
Notes: Latitude longitude (theta lambda)

## Slide 26: Convergence (Vortex Roll-Up)

## Slide 27: Cosine Bell Advection
Purpose: advect a solid body around the sphere

## Slide 29: Stability and Convergence of Cosine Bell Advection
10 revolutions

## Slide 30: Neighbor Query
We introduce a new stencil query to the RBF

## Slide 31: kD-Tree

## Slide 32: Fixed Grid

## Slide 33: Fixed Grid Impact

## Slide 34: Other Orderings

## Slide 37: Fixed Grid Improvements

## Slide 38: Roofline Model (Williams et al. 2009)
The roofline model predicts MAXIMUM possible performance on the hardware.
RBF-FD SpMV is only OI = 1/8 (double precision)

## Slide 39: GPU Comparison
Fermi M2070
Kepler K20

## Slide 40: Custom RK4
RK4 time-scheme:
Reusable kernels called as:

## Slide 41: One Thread per Stencil
Pros:
  All stencils have the same number of operations (perfect concurrency)
Cons:
  Threads may access disparate areas of memory
  Large stencils

## Slide 42: One Warp per Stencil
Pros:
  GPU operates in warps, so memory loads are shared
Cons:
  Only 32 threads queued per stencil on single multiprocessor

## Slide 43: Custom Kernel Performance (Keeneland M2070)

## Slide 44: ViennaCL
Started assisting on the ViennaCL project (Summer 2010)
  Extensions for rectangular matrices, ILU0, distributed SpMV + GMRES
  Integrated into RBF-FD code
  Benefit from existing optimizations for SpMV (formats)
Recently integrated into PETSc!

## Slide 45: Memory Compression (Sparse Storage)
O(2*n*N)
O(3*n*N)
O((2*n+1)*N)

## Slide 46: Single GPU

## Slide 47: Peak ELL GFLOP/sec on Single GPU
Fermi and Kepler perform the same.
Notes: Note that NVidia support for OpenCL is lacking

## Slide 48: Future Work for GPU SpMV Performance
Other Formats
  BELL, SELL, SBELL, etc.
Fewer memory loads
  Ordering
  Register packing (non-zero condensation)
More operations (Erlebacher et al. 2013)

## Slide 49: Performance Portability? Intel Phi
2013 OpenCL
Beta Driver

## Slide 50: Preliminary Data: Intel Phi

## Slide 51: Domain Decomposition
Restricted Additive Schwarz Method
Graph partitioning with METIS for load balancing (Karypis and Kumar, 1999)
  Requires symmetric adjacency matrix:

## Slide 52: Load Balancing with METIS
Load balancing impacts parallel gains:

## Slide 53: Node Ordering and Index Sets
Global Index Space
Local Index Space

## Slide 54: Data Movement for Multi-GPU

## Slide 55: Multi-CPU Weak Scaling
BEFORE (MPI_Alltoallv)
Tuned on Itasca (UMN)
  1,134 HP ProLiant blade servers
  2x quad-core Xeon 5660 (“Nehalem EP”) processors per node
N=1603 nodes
Impact on performance for fixed problem size per processor

## Slide 56: MPI Stages

## Slide 57: Multi-CPU Weak Scaling
2x-5x improvement at p=1024 processors
Larger Np per processor would hide growth
METIS load balancing fails for p=1024, n=17:
TUNING STEPS
AFTER

## Slide 58: Multi-CPU Strong Scaling
Fixed global problem size with decreasing workloads
MPI_Alltoallv is 2x faster when operating on one node. Slower otherwise.
Near linear (ideal) scaling.
BEFORE
AFTER
Notes: 2-way fat-tree network
8 cores is a leaf and communicate via shared memory.
Groups of 16 nodes connect via QDR InfiniBand to \emph{leaf switches} at the second level of the tree.
All leaf switches are in turn connected to two director nodes via 4x QDR InfiniBand.
The topology exhibits 8:1 contention between nodes of the same leaf and additional 2:1 contention between leaf switches \cite{ItascaTuning}.
Our implementation of RBF-FD does not detect or adjust to network topology, so network contention may inflate communication times. Tuning for the network topology is reserved for future work.

## Slide 59: Strong Scaling Efficiency and Communication Overlap
Efficiency:
Visible Communication Time:

## Slide 60: Achieved GFLOP/sec on Itasca

## Slide 61: Multi-CPU Summary
Strong scaling
  Scales well aside from effects of contention IB network and insufficient problem size for large p.
Weak scaling
  Code scales well for small stencil sizes.
  Larger Np necessary to hide increasing cost of communication.
Future work:
  Align messages properly for best performance
  Possible FMM approach to limit communication between subddomains (Yokota et al. 2010)

## Slide 62: Multi-GPU Communication
GPU adds transfers between hostdevice
Run two OpenCL queues
  One for SpMV[Q\B]
  One for hostdevice transfers and SpMV[B]
  Allows overlap of communication and
MPI_Alltoallv (No Overlap)
Overlapping Collective

## Slide 63: Multi-GPU Strong Scaling Cosine Bell (Keeneland M2070)
CSR Matrix with MPI_Alltoallv

## Slide 64: Multi-GPU Strong Scaling (Cascade M2070s)

## Slide 65: Multi-GPU Summary
Bottleneck on multi-GPUs of same node is avoided with overlapping queues.

## Slide 66: Conclusions
ViennaCL ELL format is appropriate for RBF-FD and achieves up to 8 GFLOP/sec (double precision) for a single SpMV (~43% of peak).
Bottleneck on I/O-Hub connecting multiple-GPUs on same node is avoided with overlapping queues.

## Slide 67: Community Outreach

## Slide 68: Survey of Technologies Used
C++
  Armadillo (http://arma.sf.net)
  ViennaCL (http://viennacl.sf.net)
  CUSP (https://code.google.com/p/cusp-library/)
  BOOST::uBLAS (http://www.boost.org/)
  METIS (http://cs.umn.edu/~metis/)
Matlab
Mathematica
OpenCL
CUDA
ParaView
NCAR Command Language (NCL) and NCAR Graphics

## Slide 69: Current and Future Work
Return to CUDA
  CUDA v5.5 features supports MPI with GPUDirect®
SpMV Improvements:
  Auto-tuned kernels with clSpMV (Su and Keutzer 2012)
    50+ GFLOP/sec when running in single precision
  New formats:
    BELL, SELL, SBELL (Su and Keutzer 2012)
    ELLPACK-R, pJDS, etc. (Kreutzer et al. 2012)
  Applications with Multi-Matrix SpMM (Erlebacher et al. 2013)
Multiple subdomains per GPU (to saturate Fermi and Kepler cards and overlap computation)

## Slide 70: Continued and Future Work II
Intel Phi vs NVidia Kepler
  Latest hardware from Nvidia?
Multi-GPU preconditioned GMRES solutions of RBF-FD for Stokes flow
  Core operation of GMRES: SpMV
  Current work is incomplete
with RBF-GA

## Slide 71: Questions?
Remember: this is research. If we had all the answers we wouldn’t be doing it.

## Slide 74: Extras

## Slide 76: RBF-GA (Preliminary Results)

## Slide 77: Keeneland Cosine Custom Kernel GFLOP/sec