## Slide 1: Multi-GPU Solutions of Geophysical PDEs with Radial Basis Function-generated Finite Differences
Evan F. Bollig
Nov 6th, 2013
499 DSL, 4:30 pm – 6:30 pm

## Slide 2: Acknowledgements
This work is supported in part by NSF awards DMS-#0934331 (FSU), DMS-#0934317 (NCAR) and ATM-#0602100 (NCAR).
Computational resources provided by:
  Keeneland Computing Facility at the Georgia Institute of Technology (NSF Contract OCI-0910735)

## Slide 3: Investigation Focus
Notes: Topics covered in this defense: a) the application of a recent numerical method (barely cuts into the numerical method domain. b) a distributed implementation of RBF-FD that runs on multi-GPUs (heavy into the hardware and software). c) neighbor query algorithm (software)

## Slide 4: Overview
Preliminaries
  Introduction to GPUs
  Introduction to RBF-FD
  Code Verification Details
A Fixed-Grid Method for RBF Methods
  Space Filling Curves and Node Ordering
  Lasting Impacts on Performance
Single GPU RBF-FD
Targeting Multi-GPU Clusters
  MPI Tuning
  Overlapping Communication and Computation
Conclusions
Notes: Introduction to RBF methods (beyond RBF-FD)?

## Slide 5: Why GPUs?
Massive parallelism
High GFLOP/sec
Fast Memory
Images courtesy of NVidia
Notes: Since the early 2000’s frequency scaling is no longer an option
Parallelism is mandatory to continue with Moore’s law.

## Slide 6: How to Target GPUs?
CUDA
  Widely used
OpenCL Language
  Functional portability (CPUs and GPUs)
  Similar model as CUDA

## Slide 7: GPU Memory Model
Notes: GPU loads memory in 128byte segments. Align on those for best register density.

## Slide 8: Target: GPU Cluster
Keeneland Initial Delivery (KID) System
  360 NVidia M2070
  240 CPUs, 12 threads each
Cascade
  32 NVidia M2070
  8 NVidia K20

## Slide 9: Multi-GPU Concerns
How to partition and distribute our problem?
Faster computation increases relative cost of communication. Can it be amortized/hidden?
Multi-GPU OpenCL requires device  host copies. Can they be hidden?

## Slide 10: What is an RBF?
A radially symmetric function centered at
Notes: Note the support parameter

## Slide 11: RBF-Interpolation
Notes: Arise by enforcing

## Slide 12: Pros/Cons of RBF Methods
Pros
  Function the same in any dimension
  Operate on unstructured meshes
  High order convergence
  Large time-steps
Cons
  Support parameter,
    Uncertainty Relation (Schaback, 1995)
    Can be overcome with RBF-QR (Fornberg and Piret, 2007), RBF-GA (Fornberg, Lehto and Powell, 2013)

## Slide 13: Stencils

## Slide 14: RBF-generated Finite Differences (RBF-FD)
Classical FD (1-D*):
*Nonsingularity lost in 2-D; compose weights across dimensions
RBF-FD (d-D):

## Slide 15: Differentiation Matrix
Sparse Matrix
  n nonzeros per row (stencil size)
  Unsymmetric (unique weights per row)
Sparse Matrix Vector (SpMV) multiply to get derivative across full domain

## Slide 16: Multiple Linear Operators
Solve for weights with LAPACK dgesv or other efficient direct solver
Analytically apply operators to the RBF or compose operators like classical FD

## Slide 17: Some Weight Operators
First and Second Derivatives:
Cartesian Gradient:
Cartesian Laplacian:

## Slide 18: RBF-FD for Time-Dependent PDEs
Assume an input grid is provided.
We focus on stencil generation, decomposition and the Application Phase.

## Slide 19: Verification
Hyperbolic form
Hyperviscosity

## Slide 20: Grids on Unit Sphere
Maximum Determinant (MD)
Icosahedral (Geodesic) Grid
Spherical Centroidal Voronoi Tessellation

## Slide 21: Hyperviscosity
Function
Terms
Scaling

## Slide 22: Cosine Bell
Formula, Input, Solution

## Slide 23: Cosine Bell Convergence
(left) HV parameter table
(left bottom) Eigenvalue before and after tiles
(right) Convergence plot

## Slide 24: Vortex Roll-Up

## Slide 25: Neighbor Query

## Slide 26: kD-Tree

## Slide 27: Fixed Grid

## Slide 28: Fixed Grid Improvements

## Slide 29: Related Work on Multi-GPU
Notes: RBF OpenMP: \cite{Kosec2008} happy with 1.85x speedup using two cores
RBF MPI: \cite{Divo2005, Divo2007, Ingber2003,Ingber2004,Yokota2010}
Divo and Kassab: 10 compute nodes, then 36. Solving conjugate heat transfer problems.
Ingber: 3D diffusion equations up to 64 nodes
Yokota: RBF interpolation as component of PDE solve
RBF CUDA: \cite{Schmidt2009a,Schmidt2009b,Gumerov2007a, Gumerov2007b}
Schmidt global rbf collocation (dense matrix)
Gumerov rbf interpolation inside FMM method (dense matrix)

## Slide 30: Domain Decomposition
Equivalent

## Slide 31: Load Balancing with METIS

## Slide 32: Why use the GPU?
Performance success stories from Kepler/Fermi
High TFLOP/sec count

## Slide 33: OpenCL
Comparison to CUDA
Functional Portability
Work items, work-groups, NDRange (NVIdia OpenCL manual)

## Slide 34: OpenCL vs CUDA
Diagram from Prospectus comparing hardware levels

## Slide 35: Custom Kernels
RK4 design
  Eval + Advance
  Input to each kernel

## Slide 36: Vortex Performance (Keeneland)

## Slide 37: Cosine Bell Performance
Adds one SpMV operation, but does not double performance. Question is why?

## Slide 38: Roofline Model
The roofline model predicts MAXIMUM possible performance based on the operational intensity
SpMV is only OI(1/4)

## Slide 39: How do we improve Memory-Bound Applications?
More memory compression
  ELL format
  BELL, SELL, SBELL
Fewer memory loads
  Ordering
  Register packing (non-zero condensation)
More operations (cite Erlebacher, Saule, Flyer, Bollig)

## Slide 40: Memory Compression (Format Comparison)
Figure comparing formats
Give expressions for the number of memloads

## Slide 41: Performance Comparison
N=50 format comparison figure
ELL comparison figure
Any data to compare to in related work (Rupp?, clSpMV)

## Slide 42: Future Improvements for Single GPU
clSpMV formats show potential to get 50+GFLOPs when running in single precision
What is the translation to double precision (FERMI and K20)

## Slide 44: Performance Portability? Intel Phi
High level intel phi architecture diagram
Achieved

## Slide 45: Intel Phi Comparison
Achieved GFLOP/sec on Intel Phi

## Slide 46: Performance Expectations for the GPU

## Slide 47: Achieved Performance
Cosine Bell and Vortex Roll-up

## Slide 48: SpMV Optimizations
VCL Data

## Slide 49: Decomposition
RAS

## Slide 50: Index Sets and Ordering

## Slide 51: Load Balancing

## Slide 52: METIS

## Slide 53: Overlap

## Slide 54: Limitations of I/O Hubs

## Slide 55: Achieved GFLOP/sec

## Slide 56: Conclusions

## Slide 57: Community Outreach

## Slide 58: Current and Future Work
Return to CUDA
  CUDA v5.5 features supports MPI with GPUDirect®
SpMV Improvements:
  Auto-tuned kernels with clSpMV (Su and Keutzer 2012)
  New formats:
    BELL, SELL, SBELL (Su and Keutzer 2012)
    ELLPACK-R, pJDS, etc. (Kreutzer et al. 2012)
  Applications with Multi-Matrix SpMM (Erlebacher et al. 2013)
Multiple subdomains per GPU (to saturate Fermi and Kepler cards and overlap computation)

## Slide 59: Continued and Future Work II
Intel Phi vs NVidia Kepler
  Latest hardware from Nvidia?
Multi-GPU preconditioned GMRES solutions of RBF-FD for Stokes flow
  Core operation of GMRES: SpMV
  Current work is incomplete
with RBF-GA

## Slide 60: Questions?
Remember: this is research. If we had all the answers we wouldn’t be doing it.

## Slide 63: Extras

## Slide 64: RBF-GA (Preliminary Results)